## Slide 1: Motion corrected magnetic resonance image reconstruction using deep learning
Patricia Johnson and Maria Drangova
Robarts Research Institute, Western University, London Canada
No motion
With motion
Patient motion is a significant problem in MRI
  20 % of exams require a repeat scan*
  Reacquiring images is expensive
  Increases wait times
  Can lead to delayed diagnosis
Current techniques to address motion are not always available

## Slide 2: Background
MR image data is NOT acquired in image space
Acquired in frequency space (fourier domain or k-space)
Traditional reconstruction:
It has been recently demonstrated that deep neural networks can be trained to perform image reconstruction*
Fourier transform
. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
* Zhu B, Liu JZ, Cauley SF, Rosen BR, Rosen MS. Image reconstruction by domain-transform manifold learning. Nature 2018;555:487
Objective: Develop and a train a deep neural network (DNN) to reconstruct motion corrected MR images from k-space data with simulated motion artifacts

## Slide 3: Methods: Data & motion simulation
Open-source brain images*
  53 image volumes, 128 slices per volume = 1000’s of unique 2D images
Motion profiles are randomly generated
  constraints to keep motion realistic
A unique 3D motion profile is applied to every image
* Forstmann BU, Keuken MC, Schafer AS, Bazin P, Alkemade A, Turner R (2014) Multi-modal ultra-high resolution structural 7-Tesla MRI data repository. Scientific Data 1:14005

## Slide 4: Network architecture
Motion corrupted
k-space
Reshape
& up-sample
Flatten k-space:
Input layer
64 feature maps
64 feature maps
64 feature maps
Fully-connected layer
4 Layers of convolution
output
Training: 3000 2D images
Trained on 4 12 Gb GPUs on SHARCNET (compute canada cluster)
Test: 100 2D images

## Slide 5: Results
with motion motion corrected ground truth
The trained model successfully performs motion corrected reconstruction on images with simulated motion