## Slide 1: Node-level architecture
Memory hierarchy

## Slide 2: Von Neumann bottleneck reloaded DRAM gap
Main memory access speed not sufficient to keep CPU busy…
 Introduce fast on-chip caches, holding copies of recently used data items
Approx. 10 F/B

## Slide 3: Schematic view of modern memory hierarchy & cache logic
CPU/Arithmetic unit issues a LOAD request to transfer a data item to a register
Cache logic automatically checks all cache levels if data item is already in cache.
If data item is in cache (“cache hit”) it is loaded to register.
If data item is in no cache level (“cache miss”) data item is loaded from main memory and a copy is held in cache.

## Slide 4: Memory hierarchies Effective Bandwidths
Hardware: Quantities to characterize the quality of a memory hierarchy:
Latency (Tl): Set up time for data transfer from source (e.g. main memory or caches) to destination (e.g. registers).
Bandwidth (b): Maximum amount of data per second which can be transferred between source (e.g. main memory or caches) and destination (e.g. registers).
Application: Transfer time (T) and effective bandwidth (beff) depend on data volume(V) to be transferred:
Transfer time:
Effective bandwidth:
  “Low” data volume :
  “Large” data volume :

## Slide 5: Node-level architecture
Caches – Basics

## Slide 6: Memory hierarchies The latency problem
Main memory latency and bandwidth for modern multicore CPUs: Tl = 64 ns & b = 64 GB/s
Data access is organized in cache lines (CL) – always a full CL is transferred
Multiple CLs can be loaded concurrently
  Multiple data requests by application code
  Automatic hardware prefetching
V | Tl | V/b | T | beff
8 B | 64 ns | 0.125 ns | 64.125 ns | 0.13 GB/s
128 B | 64 ns | 2 ns | 66 ns | 1.9 GB/s
4096 B | 64 ns | 64 ns | 128 ns | 32 GB/s
V=64B or V=128B on modern architectures

## Slide 7: Memory hierarchies Cache lines
If one data item is loaded from main memory (“cache miss”), whole cache line it belongs to is loaded
Cache lines are contiguous in main memory, i.e. “neighboring“ items can then be used from cache
do i=1,n
s = s + a(i)*a(i)
enddo
Iteration
LD
Cache miss : Tl
Use data
1
LD
LD
LD
2
3
4
t
LD
5
6
7
8
Use data
Use data
Use data
Use data
LD
LD
Use data
Use
Cache line size: 4 words

## Slide 8: Memory hierarchies (Automatic) Prefetching
Prefetching data to hide memory latencies of CL transfers
do i=1,n
s = s + a(i)*a(i)
enddo
Iteration
LD
Cache miss : Tl
Use data
1
LD
LD
LD
2
3
4
t
LD
5
6
7
8
Use data
Use data
Use data
Use data
LD
LD
Use data
Use
LD
Use data
LD
LD
Use data
Use
Data transfer is started before cache miss  Prefetching

## Slide 9: Memory Hierarchies Prefetching – Hide memory latency
Prefetch (PFT) instructions (limited use on modern architectures): Transfer one cache line from memory to cache and then issue LD to registers
Most architectures (Intel/AMD x86, IBM Power) use hardware-based automatic prefetch mechanisms
  HW detects regular, consecutive memory access patterns (streams) and prefetches at will
  Intel x86: Adjacent cache line prefetch loads 2 (64-byte) cache lines on L3 miss  Effectively doubles line length on loads (typical. enabled in BIOS)
  Intel x86: Hardware prefetcher: Prefetches complete page (4 KB) if 2 successive CLs in this page are accessed
For regular data access main memory latency is not an issue!
May generate excessive data transfers for irregular access pattern

## Slide 10: Node-level architecture
Data access  locality

## Slide 11: Memory Hierarchies Cache line  Spatial locality
Cache line features
  Cache line use is optimal for contiguous access (“stride 1”)  STREAMING
  Non-consecutive access reduces performance
  Access with wrong stride (e.g. cache line size) can lead to disastrous performance breakdown
“Spatial locality”: Ensure accesses to “neighboring” data items
do i=1,n
s = s + a(i)*a(i)
enddo
do i=1,n,2
s = s + a(i)*a(i)
enddo
GOOD (“Streaming”)
BAD (“Strided”)

## Slide 12: Memory Hierarchies Spatial locality & data layout
How to traverse multidimensional arrays?!
Example: Initialize matrix A with A(i,j) = i*j
What is the storage order of multidimensional-data structure?
It depends, e.g. 2-dimensional 3x3 array A of doubles
FORTRAN: column by column („column major order“)
C/C++: row by row („row major order“)
A(1,1) | A(2,1) | A(3,1) | A(1,2) | A(2,2) | A(3,2) | A(1,3) | A(2,3) | A(3,3)
0 B Memory layout 71 B
A[0][0] | A[0][1] | A[0][2] | A[1][0] | A[1][1] | A[1][2] | A[2][0] | A[2][1] | A[2][2]
0 B Memory layout 71 B

## Slide 13: Memory Hierarchies Spatial locality & data layout
Default layout for FORTRAN: column by column (column major order)
do j=1,n do i=1,n a(j,i)=i*j enddo enddo
FORTRAN:
Inner loop must access innermost/left array index
Data arrangement is “transpose” of the “usual” matrix layout
do i=1,n do j=1,n a(j,i)=i*j enddo enddo
Stride n access!
Continuous access!

## Slide 14: Memory Hierarchies Spatial locality & data layout
Default layout for C/C++: row by row (row major order)
for(j=0; j<N; ++j) { for(i=0; i<N; ++i) { a[i][j] = i*j; } }
for(i=0; i<N; ++i) { for(j=0; j<N; ++j) { a[i][j] = i*j; } }
Stride N access!
Continuous access!
C/C++:
Inner loop must access outermost/rightmost array index

## Slide 15: Memory hierarchies Temporal locality
Temporal locality: If data is already in cache - reuse it from there!
Example: Dense matrix vector multiplication (assume that cache is large enough to hold y(1:R) )
A(r,c)
do c = 1 , C
tmp=x(c)
do r = 1 , R
y(r)=y(r) + A(r,c)* tmp
enddo
enddo
x(c) stays in register
A(,):continuous access  Spatial locality
y(1:R) is loaded C times
 Temporal locality for C-1 accesses

## Slide 16: Node-level architecture
Cache management

## Slide 17: Memory Hierarchies Cache Mapping
Pairing of memory addresses with cache locations
Where is the CL to given memory addressed placed in the cache?
Simplest strategy: Directly Mapped caches, e.g. if cache size is 1 MB choose “lowest” 20 bits of memory address
Mapping substantially impacts the flexibility of replacement strategies  Reduces the potential set of evict/replace locations
May incur additional data transfer ( cache thrashing) !
CL 0
CL 1
CL 2
Memory (~109 Byte)
CL 3
…
…
…
…
…
…
…
…
L2 Cache (~106 Byte)
L1 Cache (~103 Byte)
  Memory address 32 Bit: 011100100000 11110100111110 001111

## Slide 18: Memory Hierarchies Cache Mapping – Associative Caches
Set-associative cache:
  m-way associative cache of size m x n: each memory location i can be mapped to the m cache locations (“ways”) j*n+mod(i,n), j=0..m-1
  E.g.: 2-way set associative cache of size 256 KBytes:
  Number of sets: 256 KB/ 64 Byte /2 = 2048
  Memory address (32 Bit): 011100100000111 10100111110 001111
Modern processors: 4-way to 48-way associative caches
1 |  |  |  |  | ... | 128 KB
128KB+1 |  |  | CacheLine |  |  | 256 KB
“Set”
“Way”
Address within cache line

## Slide 19: Memory hierarchies Cache Mapping – Cache Thrashing
If many memory locations are used that are mapped to the same set, cache reuse can be very limited even with m-way associative caches
Warning: Using powers of 2 in the leading array dimensions of multi-dimensional arrays should be avoided! (Cache Thrashing)
If cache / m-ways are full and new data comes in from main memory, data in cache (full cache line) must be invalidated or written back to main memory Ensure spatial and temporal data locality for data access!
  011100100000111 10100111110 001111
  011100100001000 10100111110 001111
  011100100001001 10100111110 001111
double precision A(16384,16384)
A(1,1)
A(1,2)
A(1,3)

## Slide 20: Memory hierarchies Data transfers
Caches help with getting instructions and data to the CPU “fast”
How does data travel from memory to the CPU and back?
  Remember: Caches are organized in cache lines
  Only complete cache lines are transferred between memory hierarchy levels (except registers)
  Cache MISS: Load or store instruction does not find the data in a cache level  CL transfer required
Example: Array copy A(:)=C(:)
2-level (“Inclusive cache”) cache hierarchy: L1 Load MISS  L2 Load MISS  CL loaded to L2  CL loaded to L1  data loaded to register
CPU registers
Cache
Memory
CL
CL
CL
CL
LD C(1)
MISS
ST A(1)
MISS
write allocate
evict (delayed)
3 CL transfers
LD C(2..Ncl) ST A(2..Ncl)
HIT
C(:)
A(:)

## Slide 21: Memory management Caches management details
Exclusive:
Only one cache line copy in cache hierarchy
Full aggregate effective cache size
Eviction is expensive (copy back)
Lower latency: Data can be directly loaded in L1 cache
 AMD processors and Intel Skylake L3
Inclusive:
Cache line copy in all levels
Reduced effective size in outer cache levels
Cheap eviction for unmodified cache lines
Higher latency: cache lines have to load through hierarchy
 Intel processors
“Write back”: A modified cache line is evicted to the next (lower) cache/memory level before it is overwritten by new data
“Write through”: When a cache line is updated then the cache line copy in the next (lower) cache/memory level is updated as well

## Slide 22: Memory Hierarchies Typical cache configuration
 |  | Intel Xeon E5-2680 Sandy Bridge
# FP registers |  | 16
# GP registers |  | 16
L1 D | Size | 32 KB
 | Associativity | 8-way
 | local per core | 
L2 | Size | 256 KB
 | Associativity | 8-way
 | local per core | 
L3 | Size | 20 MB (shared)
 | Associativity | 20-way
 | shared across all cores | 
Same for more recent Intel architectures: Ivy Bridge, Haswell and Broadwell
SIMD
registers
Depends on core count, CPU variant, CoD mode

## Slide 23: Memory Hierarchies Intel Xeon E5 multicore processors
FP instructions throughput per core
Max. data transfer per cycle between caches
Peak main memory bandwidth
…

## Slide 24: Node-level architecture
Cache coherence

## Slide 25: Memory hierarchies Cache Coherence
Data in cache is only a copy of data in memory
  Multiple copies of same data on multiprocessor systems
  Cache coherence protocol/hardware ensure consistent data view
  Without cache coherence, shared cache lines can become clobbered:
P1
P2
Memory
C1
P1
A1, A2
C2
P2
Bus
A1, A2
A1, A2
Load A2
Write A2=0
Load A1 Write A1=0
Write-back to memory leads to incoherent data
A1, A2
A1, A2
A1, A2
C1 & C2 entry can not be merged to:
A1, A2

## Slide 26: Memory hierarchies Cache Coherence
Cache coherence protocol must keep track of cache line (CL) status
Memory
C1
P1
A1, A2
C2
P2
Bus
A1, A2
A1, A2
P1
P2
Load A1 Write A1=0:
1. Request exclusive access to CL
2. Invalidate CL in C2
3. Modify A1 in C1
Load A2
Write A2=0:
1. Request exclusive CL access
2. CL write back + Invalidate
3. Load CL to C2
4. Modify A2 in C2
C2 is exclusive owner of CL
A1, A2
A1, A2
A1, A2
A1, A2

## Slide 27: Memory hierarchies Cache Coherence
Cache coherence can cause substantial overhead
  may reduce available bandwidth
Different implementations
  Snoop: On modifying a CL, a CPU must broadcast its address to the whole system
  Directory, “snoop filter”: Chipset (“network”) keeps track of CLs’ location and state and filters coherence traffic
Directory-based can reduce pain of additional coherence traffic
Caution: Multiple processors should never write frequently to the same cache line (“false sharing”)!

## Slide 28: Node-level architecture
Basic compute node architecture
Shared Memory Nodes: UMA and ccNUMA

## Slide 29: Basic compute node architecture UMA / ccNUMA
Shared memory: Shared address space for all processors and cache contents are kept coherent automatically
Uniform Memory Architecture (UMA):
Cache-coherent Non-Uniform
Memory Architecture (ccNUMA):
Single “flat” memory: Data access times for a given data item are constant
Limited scalability in terms of main memory bandwidth
Physically distributed memory, i.e. multiple memory controllers
“Local” & “Remote” data
Good scalability / hard to program
Outdated!

## Slide 30: Basic compute node architecture ccNUMA
Single shared address space – ease of use
A(1: 1000000000)
Separate memory controllers – scalable performance
Hardware/software layers (HT/QPI): Shared address space and ensure data coherency
Where does the data end up?????
"Golden Rule" of ccNUMA: A memory page gets mapped into the local memory of
the processor that first touches it (i.e. writes to it)!

## Slide 31: Basic compute node architecture ccNUMA – Golden Rule
void dmvm(int n, int m, double *lhs, double *rhs, double *mat){
#pragma omp parallel for private(offset,c)schedule(static) { for(r=0; r<n; ++r) { offset=m*r; for(c=0; c<m; ++c) lhs[r] += mat[c + offset]*rhs[c]; } }
Dense matrix vector multiplication (dMVM)
 OpenMP parallelization?!

## Slide 32: Basic compute node architecture ccNUMA – Golden Rule
#pragma omp parallel for schedule(static) private(c) { for(r=0; r<n; ++r) for(c=0; c<m; ++c) mat[c + m*r] = …; } }
10 cores
10 cores
Parallelization of matrix data initialization
dMVM
Matrix data initialization: serial

## Slide 33: Basic compute node architecture ccNUMA – Summary
Golden rule for NUMA-aware shared memory programming!
Touch means write (not allocate) “First touch policy”
Placement is done on page basis, i.e. chunks of 4 KB or 2 MB (see OS)
Writing a single byte is sufficient to map the full page
Thread – core affinity over execution time required  Pinning
Check if memory is “clean” – OS may keep (IO) buffers  “remove” them if necessary
Linux Tools: numactl, likwid-topology, likwid-pin