## Slide 1
THERMAL TRANSPORT IN A CROSSFLOW JET SUBJECT TO A VERY STRONG
FAVORABLE PRESSURE GRADIENT
Notes: <number>

## Slide 2
Motivation and objectives
The ability to control a flow field to enhance thermal efficiency is of great importance in many industrial and engineering applications.
An important example of flow control by three-dimensional local blowing perturbations is the jet in crossflow, not only due to its fluid-dynamic complexity but also due to its technological applications; for instance, film cooling of turbine blades, chimney plumes, fuel injection, just to name a few.
Fig. : High by pass turbofan engine
(source: http://www.aircraftenginedesign.com)
Notes: <number>

## Slide 3
Flow structures in a transverse jet
T.H. New et al., Elliptic jets in cross-flow, JFM, 494,119-140 (2003)
Top entrainment
Bottom entrainment

## Slide 4
Proposed Model and Boundary Conditions
At the wall, the classical no-slip condition is imposed for velocities. Isothermal wall is prescribed for
the thermal field, which is assumed a passive scalar. The lateral boundary conditions are handled via periodicity. The pressure is weakly prescribed at the outlet plane.

## Slide 5
Flow Solver and Inflow Generation
To successfully perform the proposed DNS, a highly accurate, very efficient, and highly scalable CFD solver is required. We use PHASTA which is an open-source, parallel, hierarchic
(2nd to 5th order accurate), adaptive, stabilized (finite-element) transient analysis tool for the solution of compressible or incompressible flows
We are employing the inflow generation method devised by Araya et al.
The seminal idea of the rescaling-recycling method is to extract the flow solution (mean and fluctuating components of the velocity and thermal fields) from a downstream plane (called “recycle”) and after performing a transformation by means of scaling functions, the transformed profiles are re-injected at the inlet plane.