## Slide 1: Hands On Instructions
Single Node Optimization
IHPCSS2018

## Slide 2: Log into Bridges
We use different nodes in this session!
salloc –reservation=ihsslm -p LM -C "PH2" --mem=750GB -N 1 --ntasks 1 --cpus-per-task 20 -C PERF
Copy examples: cp –r /home/unrz139/NLPE $HOME
Copy LIKWID: cp –r /home/unrz139/Apps $HOME

## Slide 3: Which one is fastest? Which one slowest?
for (i=0; i<N; i++)
a[i] = b[i] + c[i] * d[i]
for (i=0; i<N; i++) { bx = b[i]*b[i]; cx = c[i]*c[i]; dx = d[i]*d[i];
a[i] = bx + cx*dx }
for (i=0; i<N; i++)
a[i] = b[i] + c[i] / d[i]
Arrays a,b,c,d: double
N = 80000000
N = 8000
L1: 32 kB, L2: 256 kB, L3: 50MB

## Slide 4: Test different sizes Folder NLPE/testcode
Change VECSIZE in Makefile to find size where bandwidths differ significantly (bandwidth difference >> 1000 Mbytes/s)
  When reducing VECSIZE increase ROUNDS (max: 1000)
  make VECSIZE=X ROUNDS=Y
  Run multiple times
Why does the FP rate / Bandwidth varies so much?
Can we increase FP rate / Bandwidth with compiler options?
Notes: 1800000-2000000

## Slide 5: Runtime profile
To find “hottest” function, a function profile gives a first overview
Add to CFLAGS_ICC/GCC: -pg –g -fno-inline
Use VECSIZE=1500000 and ROUNDS=1000
Run application (generates gmon.out)
gprof testcode gmon.out

## Slide 6: Compiler options
Test different compiler options (CFLAGS_ICC/_GCC)
  -O1, -O2, -O3
  -xHost (icc) /-mavx -mfma (gcc)

## Slide 7: Triangular Matrix-Vector-Multiplication Folder: NLPE/matrix_vector_mult
Enable LIKWID: source Apps/bin/source_likwid.sh (even if using PAPI)
Add PAPI or LIKWID to matrix.c to measure instructions
  Surround calls with #ifdef LIKWID_PERFMON / PAPI_PERFMON <calls> #endif
make builds different versions, select matrix_likwid/_papi
Which thread performs most instructions? Why?

## Slide 8: Triangular Matrix-Vector-Multiplication Folder: NLPE/matrix_vector_mult
Change events to measure Flops/s
Which thread does most Flops/s? Why?
How to fix the load-imbalance?