## Slide 1: Node-level architecture
Single Core Architecture

## Slide 2: Quiz
What does “clock frequency” mean in computers?
What is “memory bandwidth”?
What is SIMD vectorization?
What is ccNUMA?
The “heartbeat” of the CPU. A clock cycle is the smallest unit of time on a CPU chip. Typically < 1ns 
Rate of data transfer between main memory (RAM) and CPU chip. Typical
A[0]
A[1]
A[2]
A[3]
B[0]
B[1]
B[2]
B[3]
C[0]
C[1]
C[2]
C[3]
+
+
+
+
R0
R1
R2
Single Instruction Multiple Data. Data-parallel load/store and execution units.

## Slide 3: Quiz
What is a register?
What is Amdahl’s Law?
What is a pipelined functional unit?
A storage unit in the CPU core that can take one single value (a few values in case of SIMD). Operands for computations reside in registers.
rax
rbx
rcx
rdx
rsi
ymm0
ymm1
ymm2
ymm3
ymm4
An instruction execution unit on the core that executes an instruction in several simple sub-steps. The stages of the pipeline can act in parallel on several instructions at once.

## Slide 4: Cycle gymnastics
1 cycle or cy = smallest unit of time on a CPU (“heartbeat”)
Basic unit of work: Floating-point operation (Flop or F)
Basic unit of traffic: Byte
Unit of bandwidth: Bytes/s
  Typical memory bandwidth: 48 Gbytes/s = 4.8∙1010 Bytes/s
  How many bytes per cycle is that?
Clock speed of typical CPU: 3.0 Gcy/s (or GHz)
Typical peak performance of 8-core CPU: Ppeak = 192 GF/s
How many FLOPs per cycle per core is that?
Typical duration of a double precision multiply: 5 cycles
  How much time is that?

## Slide 5: Node-level architecture
Key single processor/core features:
Pipelining Superscalarity SingleInstructionMultipleData

## Slide 6: General-purpose cache based microprocessor core
Implements “Stored Program Computer” concept (Turing 1936)
Similar designs on all modern systems
(Still) multiple potential bottlenecks
Flexible!
Stored-program computer
Modern CPU core

## Slide 7: Basic resources on a stored program computer Instruction execution and data movement
Instruction execution
  This is the primary resource of the processor. All efforts in hardware design are targeted towards increasing the instruction throughput.
  Instructions are the concept of “work” as seen by processor designers.
  Not all instructions count as “work” as seen by application developers!
  Example: Adding two arrays A(:) and B(:)
do i=1, N A(i) = A(i) + B(i) enddo
Processor work: LOAD r1 = A(i) LOAD r2 = B(i) ADD r1 = r1 + r2 STORE A(i) = r1 INCREMENT i BRANCH  top if i<N
User work: N FLOPs (ADDs)

## Slide 8: Basic resources on a stored program computer Instruction execution and data movement
Data transfer
  Data transfers are a consequence of instruction execution and therefore a secondary resource. Maximum bandwidth is determined by the request rate of executed instructions and technical limitations (bus width, speed).
  Example: Adding two arrays A(:) and B(:)
  Crucial question: What is the „bottleneck“?
  Data transfer? Code execution?
do i=1, N A(i) = A(i) + B(i) enddo
Data transfers: 8 byte: LOAD r1 = A(i) 8 byte: LOAD r2 = B(i) 8 byte: STORE A(i) = r2
Sum: 24 byte

## Slide 9: From application to microprocessor
Application: High Level Programming Language (e.g. C / C++ / Fortran) - portable
Compiler translates program to Instruction set (architecture) (IA32, IA64)
Hardware specific execution of Instruction Set Architecture (ISA)
Computer
Control Unit
Mem
ALU
I/O
Instruction Set
Compiler
Application
sum=0.0
do i=1, N sum=sum + A(i) enddo …
Up to 24 x performance

## Slide 10: From application to microprocessor
sum=0.d0
do i=1, N sum = sum + A(i) enddo …
Baseline address of A(i)
sum in register xmm1
N in register rax
ADDSD: Add 1st argument to 2nd argument and store result in 2nd argument
Compiler
Jump to label ..B1.62 if loop continues
Register increment
Compare register content
i in register rdx

## Slide 11: Node-level architecture
Microprocessors – Pipelining

## Slide 12: Pipelining of arithmetic/functional units
Idea:
  Split complex instruction into several simple / fast steps (stages)
  Each step takes the same amount of time, e.g., a single cycle
  Execute different steps on different instructions at the same time (in parallel)
Benefits:
  Core can work on 5 independent instructions simultaneously
  One instruction finished each cycle after the pipeline is full
Drawback:
  Pipeline must be filled; large number of independent instructions required
  Requires complex instruction scheduling by hardware (out-of-order execution) or compiler (software pipelining)
Pipelining is widely used in modern computer architectures

## Slide 13: Interlude: Possible stages for multiply
Real numbers can be represented as mantissa and exponent in a “normalized” representation, e.g.: s*0.m * 10e with
  Sign s={-1,1}
  Mantissa m which does not contain 0 in leading digit
  Exponent e some positive or negative integer
Multiply two real numbers r1*r2 = r3: s1*0.m1 * 10e1 * s2*0.m2 * 10e2
(s1*s2)* (0.m1*0.m2) * 10(e1+e2)
s3 * 0.m3 * 10e3

## Slide 14: 5-stage Multiplication-Pipeline: A(i)=B(i)*C(i); i=1,...,N
1
B(1)
C(1)
2
B(2)
C(2)
B(1)
C(1)
3
B(3)
C(3)
B(2)
C(2)
B(1)
C(1)
4
B(4)
C(4)
B(3)
C(3)
B(2)
C(2)
A(1)
5
B(5)
C(5)
B(4)
C(4)
B(3)
C(3)
A(2)
A(1)
6
B(6)
C(6)
B(5)
C(5)
B(4)
C(4)
B(3)
C(3)
A(2)
...
...
...
...
...
...
Cycle:
Separate
Mant. / Exp.
Mult.
Mantissa
Add.
Exponents
Normal.
Result
Insert Sign
Stage
N
B(N)
C(N)
B(N-1)
C(N-1)
B(N-2)
C(N-2)
B(N-3)
C(N-3)
A(N-4)
N+1
B(N)
C(N)
B(N-1)
C(N-1)
B(N-2)
C(N-2)
A(N-3)
N+2
B(N)
C(N)
B(N-1)
C(N-1)
A(N-2)
N+3
B(N)
C(N)
A(N-1)
N+4
B(N)
C(N)
Wind-up
Wind-down
First result is available after 5 cycles (=latency of pipeline)!
Empty pipeline stages in Wind-up/-down phase!

## Slide 15: Pipelining: Speed-Up and Throughput
Assume m-stage pipe, i.e. pipeline depth is m and fixed clock speed
Speed-up of pipelined () vs. non-pipelined () execution time
Throughput of fully piplined execution of N instructions, i.e. average instructions completed per cycle:
Large N limits:
Speed-Up: for
Throughput: for

## Slide 16: Pipelining: Beyond multiplication
Typical number of pipeline stages on modern CPUs:
  2-5 for most (important) hardware pipelines: LoaD; STore; MULT; ADD
  >>10 for other floating point pipelines: DIVide/SQuareRooT
  Many other piplined ALUs, e.g. integer arithmetics
Most “older” x86 processors (AMD, Intel): 1 MULT & 1 ADD floating point unit per processor core  Max. 1 MULT & 1 ADD instruction per cycle

## Slide 17: Pipelining: Beyond multiplication
Latest Intel (Haswell+) & AMD (Interlagos+): 1 (AMD) or 2 Floating Point Fused MultiplyAdd (FMA) units
  FMA3 instruction: s= s + a*b  1 Input register (s) is overwritten
  FMA4 instruction: s= r + a*b  No input register is modified
 Max. 2 (1) FMA instruction per cycle for Intel (AMD) processors

## Slide 18: Costs of arithmetic instructions Intel SandyBridge
Consequence: Avoid expensive instructions in hot spots!
Instruction | Latency [cy/instruction] | Throughput [instruction/cy]
ADD DP (SP) | 3 (3) | 1 (1)
MULT DP (SP) | 5 (5) | 1 (1)
SQRT DP | 45 | 1/44 = 0.023
SQRT SP | 29 | 1/28 = 0.036
DIV DP | 45 | 1/44 = 0.023
EXP DP | 83 | 1/83 = 0.012
SIN DP | 79 | 1/79 = 0.013
Latency [cycles/instruction] Depth of pipeline, i.e.
cycles to execute a single instruction (worst case)
Throughput [instruction/cycle] Cycles per instruction
if pipeline is full (best case: 1 instruction/cycle)
Instructions
Library calls
(glibc 2.12)

## Slide 19: Pipelining: Potential problems Data dependencies
…
for(int i=1; i<n; ++i)
a[i] = a[i-1] + s;
…
…
for(int i=1; i<n; ++i)
a[i] = a[i] + s;
…
1 floating point
operation (1 F)
per iteration
a[5]=a[5]+s
a[4]=a[3]+s
a[3]=a[2]+s
a[1]=a[0]+s
a[2]=a[1]+s
Performance model:
Code: 1 F / 3 cy
Hardware: 3.5 GHz (3.5 Gcy/s)
Expect: 1.17 GF/s
a[4]=a[4]+s
a[3]=a[3]+s
a[1]=a[1]+s
a[2]=a[2]+s
Performance model:
Code: 1 F / 1 cy
Hardware: 3.5 GHz (3.5 Gcy/s)
Expect: 3.5 GF/s

## Slide 20: Pipelining: Potential problems Data dependencies
Sometimes dependencies are not obvious!
What about “reduction operations”?
Data (register) dependency on sum (%xmm1)  1 F / 3 cy for above code!
sum=0.d0
do i=1, N sum=sum + A(i) enddo …
A(i) (incl. LD)
sum in register xmm1
i (loop counter)
N
ADD 1st argument to 2nd argument and store result in 2nd argument

## Slide 21: Pipelining: Potential problems Subroutine/function calls within a loop
 Inline subroutines! (can be done by compiler….)
do i=1, N call elementprod(A(i),B(i), psum) C(i)=psum enddo … function elementprod( a, b, psum) … psum=a*b
do i=1, N psum=A(i)*B(i) C(i)=psum enddo …

## Slide 22: The Instruction pipeline
Besides arithmetic & functional unit, instruction execution itself is pipelined also, e.g.: one instruction performs at least 3 steps:
Fetch Instruction from L1I
Decode instruction
Execute Instruction
Hardware Pipelining on processor (all units can run concurrently):
Fetch Instruction 1 from L1I
Decode Instruction 1
Execute Instruction 1
Fetch Instruction 2 from L1I
Decode Instruction 2
Decode Instruction 3
Execute Instruction 2
Fetch Instruction 3 from L1I
Fetch Instruction 4 from L1I
1
2
3
4
Branches can stall this pipeline! (Speculative Execution, Predication)
Each Unit is pipelined itself (cf. Execute=Multiply Pipeline)
Time (cycles)

## Slide 23: The Instruction pipeline: Problem Unpredictable branches to other instructions
Fetch Instruction 1 from L1I
Decode Instruction 1
Execute Instruction 1
Fetch Instruction 2 from L1I
Decode Instruction 2
Decode Instruction 3
Execute Instruction 2
Fetch Instruction 3 from L1I
1
2
3
4
Assume: Result determines next instruction!
Time (cycles)
5
6
7
8

## Slide 24: Node-level architecture
Microprocessors – Superscalarity

## Slide 25: Superscalar Processors
Superscalar processors provide additional hardware (i.e. transistors) to execute multiple instructions per cycle!
Parallel hardware components / pipelines are available to
  fetch / decode / issues multiple instructions per cycle
  multiple integer / address calculations per cycle
  load (store) multiple operands (results) from (to) cache per cycle
  multiple floating point instructions per cycle
Superscalar RISC processors use out-of order (OOO) execution hardware to exploit the parallel hardware (e.g. ARM)

## Slide 26: Superscalar Processors Instruction Level Parallelism
Multiple units enable use of Instrucion Level Parallelism (ILP): Instruction stream is “parallelized” on the fly
Issuing m concurrent instructions per cycle: m-way superscalar
Current: 3- to 6-way superscalar with 2 or 4 FP instructions per cycle
Fetch Instruction 4 from L1I
Decode Instruction 1
Execute Instruction 1
Fetch Instruction 2 from L1I
Decode Instruction 2
Decode Instruction 3
Execute Instruction 2
Fetch Instruction 3 from L1I
Fetch Instruction 4 from L1I
Fetch Instruction 3 from L1I
Decode Instruction 1
Execute Instruction 1
Fetch Instruction 2 from L1I
Decode Instruction 2
Decode Instruction 3
Execute Instruction 2
Fetch Instruction 3 from L1I
Fetch Instruction 4 from L1I
Fetch Instruction 2 from L1I
Decode Instruction 1
Execute Instruction 1
Fetch Instruction 2 from L1I
Decode Instruction 2
Decode Instruction 3
Execute Instruction 2
Fetch Instruction 3 from L1I
Fetch Instruction 4 from L1I
Fetch Instruction 1 from L1I
Decode Instruction 1
Execute Instruction 1
Fetch Instruction 5 from L1I
Decode Instruction 5
Decode Instruction 9
Execute Instruction 5
Fetch Instruction 9 from L1I
Fetch Instruction 13 from L1I
4-way „superscalar“
Time (cycles)

## Slide 27: Superscalar processors Executing multiple instructions concurrently
…
for(int i=1; i<n; ++i)
a[i] = a[i] + s;
…
LOAD (Latency: 4 cy)
ADD (Latency: 3cy)
STORE (Latency: 2 cy)
Cycle 1 Cycle 2 Cycle 3 Cycle 4 Cycle 5 Cycle 6 Cycle 7 Cycle 8 Cycle 9 Cycle 10 Cycle 11 Cycle 12 Cycle 13 Cycle 14 Cycle 15 Cycle 16 …
load a[1] load a[2] load a[3] load a[4] load a[5] add a[1]=c,a[1] load a[6] add a[2]=c,a[2] load a[7] add a[3]=c,a[3] load a[8] add a[4]=c,a[4] store a[1] load a[9] add a[5]=c,a[5] store a[2] load a[10] add a[6]=c,a[6] store a[3] load a[11] add a[7]=c,a[7] store a[4] load a[12] add a[8]=c,a[8] store a[5] load a[13] add a[9]=c,a[9] store a[6] load a[14] add a[10]=c,a[10] store a[7] load a[15] add a[11]=c,a[11] store a[8] load a[16] add a[12]=c,a[12] store a[10] … … …
“Steady state:”
3 instructions/cy (“3-way superscalar”)
Correct interleaving / reordering the instruction streams:
Out-Of-Order (OOO) execution
  Instructions Per Cycle: IPC=3
  Cycles Per Instruction: CPI=0.33

## Slide 28: Superscalar processors Intel x86 processors – qualitative view
Max. of 4 instr./cycle can
be decoded  CPI ≥ 0.25
FP MULT & FP ADD can run in parallel
3 LD/ST units
2 memory instr.
Concurrently
(AGU)
Execution ports map
decoded instructiona
to execution units
Intel SandyBridge/IvyBridge

## Slide 29: Superscalar processors Intel x86 processors – qualitative view
Max. attainable performance
(,, registers)
Peak Performance 1 ST + 1 FMA + 1 LD  1 cy
Peak Performance 1 ST + 1 LD + 1 MULT  1 cy
Peak Performance 1 ST + 1 FMA + 3 LD  1.5 cy
Per cycle (cy) a maximum of
  2 LOAD (LD) AND 1 STORE (ST) instruction
  2 floating point instructions (Port0/1): Any combination of FMA, MULT, ADD
  4 instructions in total
Peak performance: 2 FMA / cy
Peak Performance: (1 MULT + 1 ADD) / cy
Port 0
Port 1
Port 5
Port 2
Port 3
Port 4
Port 6
Port 7
ALU
ALU
ALU
FMA
FMA
FSHUF
JUMP
LOAD
LOAD
AGU
AGU
STORE
AGU
FMUL
ALU
JUMP
Intel Haswell/Broadwell

## Slide 30: Superscalar processors Summary
Exploits Instruction Level Parallelism
Obstacles:
  Instruction / Loop carried dependencies
  Latencies
Enabling Techniques
  Software Pipelining & Loop unrolling (see later) (Compile Time)
  Out-of-order Execution (Runtime)
  Simultaneous Multithreading (Runtime)
See later

## Slide 31: Node-level architecture
Microprocessors – Single Instruction Multiple Data (SIMD)-processing

## Slide 32: SIMD-processing Basics
Single Instruction Multiple Data (SIMD) instructions allow the concurrent execution of the same operation on “wide” registers.
x86_64 SIMD instruction sets:
SIMD-execution  vector execution
If compiler has vectorized loop  SIMD instructions are used
SIMD version | Register width | Double precision values | Single precision values
Scalar | 64 Bit / 32 Bit | 1 | 1
SSE | 128 Bit | 2 | 4
AVX/AVX2 | 256 Bit | 4 | 8
AVX512 | 512 Bit | 8 | 16

## Slide 33: SIMD-processing Basics
Scalar execution: R2 ADD [R0,R1]
SIMD execution: R2 V64ADD [R0,R1]
64 Bit
256 Bit
A[0]
B[0]
C[0]
+
R0
R1
R2
A[0]
A[1]
A[2]
A[3]
B[0]
B[1]
B[2]
B[3]
C[0]
C[1]
C[2]
C[3]
+
+
+
+
R0
R1
R2
33
If 128 Bit SIMD instructions (SSE) are executed only half of the registers width is used

## Slide 34: SIMD-processing Basics
void scale_shift(double *A, double *B, double *C, int n) {
for(int i=0; i<n; ++i)
C[i] = A[i] + B[i] + C[i-1];
}
No SIMD-processing for loops with data dependencies
“Pointer aliasing” may prevent compiler from vectorization
If “pointer aliasing” is not used, tell it to the compiler
Intel: –fno-alias GCC: -fargument-noalias
#pragma simd enforces vectorization (Intel > 12.0)
Intel compiler will vectorize starting with –O2. To enable specific SIMD extensions use the –x option:
  -xSSE2 vectorize for SSE2 capable machines
  -xAVX on Sandy/Ivy Bridge processors
  -xCORE-AVX2 on Haswell/Broadwell
  -xCORE-AVX512 on Skylake (certain models)
  -xMIC-AVX512 on Xeon Phi Knights Landing
  -xHOST use SIMD extensions of machine you compile on
Prerequesites:
Countable loop
Innermost loop
Single entry and single exit
No function calls & straight line code

## Slide 35: SIMD-processing Data layout: structure of arrays
float *A,*B,*C,*D,*R;
+ / √
+ / √
+ / √
+ / √
xmm0
xmm1
xmm2
xmm3
A[]
B[]
C[]
D[]
R[]

## Slide 36: SIMD-processing Data layout: array of structures
xmm0
S[]
+
/
√
xmm1
struct stype {
float A,B,C,D,R;
};
struct stype *S;
Things to watch out for:
LOADs, STOREs, arithmetic all need to be SIMD-parallel
“Horizontal” operations across slots of a register are slow (no good support in instruction sets)
A (limited) number of parallel data streams are not a problem

## Slide 37: SIMD-processing Basic rules
Rules for vectorizable loops
Inner loop
Countable (loop length can be determined at loop entry)
Single entry and single exit
Straight line code (no conditionals)
No (unresolvable) read-after-write data dependencies
No function calls (exception intrinsic math functions)
Better performance with:
Simple inner loops with unit stride (contiguous data access)
SIMD-compatible data layout
Minimize indirect addressing
Align data structures to SIMD width boundary
In C use the restrict keyword and/or const qualifiers and/or compiler options to rule out array/pointer aliasing

## Slide 38: Expensive instructions With SIMD
Instruction | Latency [cy/instruction] | Throughput [instruction/cy] | Operation Throughput [operations/cy]
ADD DP (SP) | 3 (3) | 1 (1) | 4 (8)
MULT DP (SP) | 5 (5) | 1 (1) | 4 (8)
SQRT DP | 45 | 1/44 = 0.023 | 1/11 = 0.091
SQRT SP | 29 | 1/28 = 0.036 | 1/7 = 0.143
DIV DP | 45 | 1/44 = 0.023 | 1/11 = 0.091
EXP DP | 83 | 1/83 = 0.012 | 1/12.5 = 0.080
SIN DP | 79 | 1/79 = 0.013 | 1/17.5 = 0.057
Intel SandyBridge
SIMD (256-Bit AVX)
Consequence: Avoid expensive instructions like the plague!
glibc 2.12
Intel SVML

## Slide 39: SIMD-processing Summary
Exploits Data Parallelism
Obstacles:
  Loop carried dependencies
  Non-vectorizable parts (e.g. non-consecutive data access)
Enabling Techniques
  Avoid / resolve data dependencies
  (Inner) Loop Unrolling + SIMD instructions (Compile Time)
  Data layout / alignment for better performance

## Slide 40: Single core peak performance Putting it all together
Floating point (FP) peak performance of modern cores depends on
Pipelining  1 FP instruction per cycle per execution unit
Superscalarity  Multiple FP instructions per cycle
SIMD vectorization  Multiple FP operations per instructione
FMA factor  FMA instructions or MULT/ADD only
Clock speed  cycles / s

## Slide 41: Single core peak performance Putting it all together
Maximum floating point (FP) performance:
Super-
scalarity
FMA
factor
SIMD
factor
Clock
Speed
Typical representatives | [inst./cy] |  | [F/inst.] |  | Code | [GHz] | [GF/s]
Nehalem | 2 | 1 | 2 | Q1/2009 | X5570 | 2.93 | 11.7
Westmere | 2 | 1 | 2 | Q1/2010 | X5650 | 2.66 | 10.6
Sandy Bridge | 2 | 1 | 4 | Q1/2012 | E5-2680 | 2.7 | 21.6
Ivy Bridge | 2 | 1 | 4 | Q3/2013 | E5-2660 v2 | 2.2 | 17.6
Haswell | 2 | 2 | 4 | Q3/2014 | E5-2695 v3 | 2.3 | 36.8
Broadwell | 2 | 2 | 4 | Q1/2016 | E5-2699 v4 | 2.2 | 35.2
IBM POWER8 | 2 | 2 | 2 | Q2/2014 | S822LC | 2.93 | 23.4
Typical representatives |  |  |  |  | Code |  | 
Nehalem | 2 | 1 | 2 | Q1/2009 | X5570 | 2.93 | 11.7
Westmere | 2 | 1 | 2 | Q1/2010 | X5650 | 2.66 | 10.6
Sandy Bridge | 2 | 1 | 4 | Q1/2012 | E5-2680 | 2.7 | 21.6
Ivy Bridge | 2 | 1 | 4 | Q3/2013 | E5-2660 v2 | 2.2 | 17.6
Haswell | 2 | 2 | 4 | Q3/2014 | E5-2695 v3 | 2.3 | 36.8
Broadwell | 2 | 2 | 4 | Q1/2016 | E5-2699 v4 | 2.2 | 35.2
IBM POWER8 | 2 | 2 | 2 | Q2/2014 | S822LC | 2.93 | 23.4